| ILLUSTRATED REPORT FOR BRILLIANT |  |  | Parameter | Avg | Min | Max | Dev | Cut | Sym |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Polished Brilliant |  |  |  | Diameter, mm | 5.763 | 5.755 | 5.769 | 0.24% | E | EX |  |  | 5.765 | 5.763 | 5.763 | 5.765 |  |  |  |  |
|  |  |  |  | Crown angle, ° | 36.32 | 36.27 | 36.40 | 0.13 | Grading | EX |  |  | 36.29 | 36.33 | 36.34 | 36.31 | 36.33 | 36.27 | 36.40 | 36.28 |
|  |  |  |  | Pavilion angle, ° | 41.18 | 41.11 | 41.26 | 0.15 | Grading | EX |  |  | 41.15 | 41.19 | 41.26 | 41.18 | 41.21 | 41.23 | 41.13 | 41.11 |
| Model | Simple |  |  | Total height, % | 62.29 |  |  |  | E |  |  |  |  |  |  |  |  |  |  |  |
| Expert name | Makoed A.G. |  |  | Crown height, % | 15.74 | 15.62 | 15.80 | 0.18 | E | EX |  |  | 15.62 | 15.67 | 15.74 | 15.76 | 15.79 | 15.77 | 15.78 | 15.80 |
| Report date | 18.04.2008 |  |  | Pavilion depth, % | 43.58 | 43.44 | 43.70 | 0.25 | N/A | EX |  |  | 43.68 | 43.70 | 43.65 | 43.44 | 43.48 | 43.61 | 43.52 | 43.55 |
| Real weight, ct |  |  |  | Table, % | 57.26 | 57.18 | 57.34 | 0.17 | Grading | EX |  |  | 57.34 | 57.24 | 57.27 | 57.18 |  |  |  |  |
| Calculated weight, ct | 0.73, 0.7291 |  |  | Culet, % | 0.41 | 0.37 | 0.44 | 0.07 | E | EX |  |  |  |  |  |  |  |  |  |  |
| Measurements | 5.763 (5.755-5.769) x 3.590 /0.002 mm |  |  | Girdle Bezel, % | 2.96 | 2.89 | 3.09 | 0.20 | E | EX |  |  | 2.99 | 2.91 | 2.91 | 3.09 | 3.00 | 2.89 | 2.96 | 2.95 |
| Spread | -0.02 ct, -2.96% |  |  | Girdle Bone, % | 2.97 | 2.85 | 3.27 | 0.42 |  | EX |  |  | 3.03 | 2.99 | 3.27 | 2.94 | 2.85 | 2.91 | 2.89 | 2.85 |
| AGS Spread | N/A ct, N/A% |  |  | Girdle Valley, % | 1.23 | 1.09 | 1.46 | 0.36 | E | EX |  |  | 1.22 | 1.18 | 1.24 | 1.24 | 1.38 | 1.46 | 1.27 | 1.26 |
|  |  |  |  |  |  |  |  |  |  |  |  |  | 1.23 | 1.09 | 1.24 | 1.23 | 1.23 | 1.14 | 1.17 | 1.16 |
| Average values, mm |  |  | Star: | 54.74: | 54.38: | 55.16: | 0.78 | E | EX |  |  | 54.44: | 54.89: | 54.92: | 54.78: | 55.16: | 54.38: | 54.41: | 54.92: |
|  |  |  | Upper ratio, % | 45.26 | 45.62 | 44.84 |  |  |  |  |  | 45.56 | 45.11 | 45.08 | 45.22 | 44.84 | 45.62 | 45.59 | 45.08 |
| Diam | Total height | Crown height | Pav. depth | Table | Culet | Girdle |  |  | Star angle, ° | 24.02 | 23.86 | 24.12 | 0.26 |  | EX |  |  | 23.86 | 24.08 | 24.10 | 24.03 | 24.00 | 23.98 | 24.12 | 24.00 |
|  |  |  |  |  |  | Bezel | Bone | Valley |  |  | Upper girdle angle, ° | 43.82 | 43.35 | 44.42 | 1.07 |  | VG |  |  | 43.45 | 43.65 | 43.98 | 44.16 | 43.35 | 43.39 | 44.14 | 44.42 |
| 5.763 | 3.590 | 0.907 | 2.511 | 3.300 | 0.024 | 0.171 | 0.171 | 0.071 |  |  |  |  |  |  |  |  |  |  |  | 43.81 | 44.17 | 43.62 | 43.59 | 43.56 | 43.93 | 43.76 | 44.14 |
|  |  |  |  |  |  |  |  |  |  |  | Length girdle facet, % | 79.78 | 78.94 | 80.47 | 1.53 | E | EX |  |  | 80.47 | 80.10 | 79.81 | 79.63 | 79.88 | 79.85 | 79.42 | 78.94 |
|  |  |  |  |  |  |  |  |  |  |  |  | 79.90 | 79.41 | 79.66 | 80.33 | 80.20 | 79.91 | 79.21 | 79.82 |
|  |  |  | Lower girdle angle / Halves angle, ° | 42.29 | 42.18 | 42.37 | 0.20 |  | EX |  |  | 42.26 | 42.31 | 42.33 | 42.37 | 42.34 | 42.31 | 42.33 | 42.35 |
|  |  |  |  |  |  |  |  |  |  |  |  | 42.33 | 42.37 | 42.34 | 42.25 | 42.18 | 42.20 | 42.19 | 42.24 |
|  |  |  | Twist, ° | 0.36 | 0.09 | 0.73 | 0.63 |  | EX |  |  | 0.38 | 0.73 | 0.30 | 0.35 | 0.09 | 0.46 | 0.25 | 0.34 |
|  |  |  | Crown height, mm | 0.907 | 0.900 | 0.911 | 0.010 | E | EX |  |  | 0.900 | 0.903 | 0.907 | 0.908 | 0.910 | 0.909 | 0.910 | 0.911 |
|  |  |  | Pavilion depth, mm | 2.511 | 2.504 | 2.518 | 0.015 | N/A | EX |  |  | 2.517 | 2.518 | 2.515 | 2.504 | 2.506 | 2.513 | 2.508 | 2.510 |
|  |  |  | Table, mm | 3.300 | 3.295 | 3.305 | 0.010 | Grading | EX |  |  | 3.305 | 3.299 | 3.300 | 3.295 |  |  |  |  |
|  |  |  | Culet, mm | 0.024 | 0.021 | 0.025 | 0.004 | E | EX |  |  |  |  |  |  |  |  |  |  |
|  |  |  | Girdle Bezel, mm | 0.171 | 0.166 | 0.178 | 0.012 | E | EX |  |  | 0.173 | 0.168 | 0.167 | 0.178 | 0.173 | 0.166 | 0.170 | 0.170 |
|  |  |  | Girdle Bone, mm | 0.171 | 0.164 | 0.188 | 0.024 |  | EX |  |  | 0.175 | 0.172 | 0.188 | 0.169 | 0.164 | 0.168 | 0.167 | 0.164 |
|  |  |  | Girdle Valley, mm | 0.071 | 0.063 | 0.084 | 0.021 | E | EX |  |  | 0.070 | 0.068 | 0.071 | 0.072 | 0.080 | 0.084 | 0.073 | 0.072 |
|  |  |  |  |  |  |  |  |  |  |  |  | 0.071 | 0.063 | 0.071 | 0.071 | 0.071 | 0.066 | 0.067 | 0.067 |
|  |  |  | Measurement as per OctoNus theory: |  |  |  |
|  |  |  | Crown angle, ° | 36.32 | 36.29 | 36.37 | 0.07 |  |  |  |  | 36.31 | 36.30 | 36.37 | 36.29 |  |  |  |  |
|  |  |  | Pavilion angle, ° | 41.18 | 41.15 | 41.21 | 0.06 |  |  |  |  | 41.18 | 41.21 | 41.19 | 41.15 |  |  |  |  |
|  |  |  | Fish eye effect, ° | 9.55 | N/A |  |  |  | Extra Facet / Nat | No |
|  |  |  | Culet through Crown Bezel, ° | 7.06 | N/A |  |  |  | Girdle to MIC, mm | 0.002 |
|  |  |  | Parameter, ° | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  | Paint / Dug | Avg | Type | Sym | Dev | Sym |
|  |  |  | Pav. azimuths dev. from ideal | 0.00 | -0.13 | -0.05 | -0.05 | 0.04 | -0.08 | 0.09 | 0.01 |  |  | Crown, ° | -0.09 |  | EX | 0.79 | EX |
|  |  |  | Crown azimuths dev. from ideal | 0.38 | 0.60 | 0.25 | 0.29 | 0.13 | 0.38 | 0.34 | 0.35 |  |  | Crown, notch. | 0.0, Negligible |  |  | 0.2 |  |
|  |  |  | Crown painting | -0.70 | -0.19 | 0.07 | -0.04 | -0.47 | -0.66 | 0.36 | 0.79 |  |  | Pavilion, ° | 0.12 |  | EX | 0.48 | EX |
|  |  |  |  | -0.35 | 0.32 | -0.28 | -0.43 | -0.37 | 0.31 | -0.47 | 0.70 |  |  | Pavilion, notch. | 0.0, Negligible |  |  | 0.1 |  |
|  |  |  | Pavilion painting | 0.08 | -0.03 | 0.30 | -0.17 | 0.07 | 0.30 | 0.15 | 0.48 |  |  |  |
|  |  |  |  | 0.09 | -0.04 | 0.42 | 0.25 | -0.05 | 0.27 | -0.17 | -0.08 |  |  |  |
| Appraiser title | GIA_PCTG_StarCul |  |  |  |  |  |  |  |
| Overall cut quality | E |  |  |  |  |  |  |  |
| Symmetry appraiser title | Internal |  |  |  |  |  |  |  |
| Overall symmetry quality | VG |  |  |  |  |  |  |  |
| Color |  |  |  |  |  |  |  |  |
| Clarity |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Girdle center |  | Culet center |  | Тable center |  |  |  |
| Polish |  |  |  | Offset by table axis |  |  |  |
|  |  |  |  | Girdle-Culet | 0.20 ± 0.22, % | 0.012 ± 0.013, mm |  |  |  |
| Fluorescence |  |  |  | Girdle-Table | 0.11 ± 0.20, % | 0.006 ± 0.011, mm |  |  |  |
|  |  |  |  | Table-Culet | 0.19 ± 0.24, % | 0.011 ± 0.014, mm |  |  | Girdle to table-culet line offset | 0.11 %, 0.006 mm |